NetinoFastPath
Performance results

# Specifications
NFP/ODP specifications:
ODP version	ODP-DPDK v1.34.0.0_DPDK_19.11
ODP configuration	--enable-dpdk / --enable-dpdk-zero-copy / --with-platform=linux-generic
NFP version	NFP 6.0.0
NFP configuration	--with-odp=<path to ODP install>

Platform specifications:
CPU Version	Intel(R) Xeon(R) CPU E5-2678 v3
Core Frequency / IO Frequency	2.50GHz
OS Version	Ubuntu 20.04.3 LTS
SDK Version	DPDK 20.11
NIC Interfaces	Intel 82599ES 10-Gigabit SFI/SFP+

# Use-case: IP Forwarding
## Test description
IP traffic is sent from a packet generator (node 1) to a destination (node 3) through the forwarder (node 2) running NFP application.

2
1

3

192.168.100.10	192.168.100.20, 192.168.200.10	192.168.200.20

## Configurations
Name	Description
Burst TX mode	Settings applied through configuration file (NFP_CONF_FILE): / nfp_global_param: { / pkt_pool: { / nb_pkts = 262143 / } / pkt_tx_burst_size = 32 / evt_rx_burst_size = 32 / }
Default configuration	No configuration file.

## Results
### Case: direct mode RX, TX
Note:
- ‘fpm_direct’ example application is used
- TX and RX operations are performed in ‘direct mode’
- RSS is enabled on RX
- Burst TX mode enabled by default

Default configuration:
IPv4 Forwarding with 64-byte frame	Throughput (mpps)
	Multi packet API	Single packet API
1 core	3.66	3.86
2 cores	13.01	13.53
3 cores	14.70	14.70

### Case: scheduler mode RX, direct mode TX
Note:
- ‘webserver2’ example application is used in mode 2 (sched_rss)
- RX operations are performed in ‘scheduled atomic mode’
- TX operations are performed in ‘direct mode’
- RSS is enabled on RX
Burst TX mode configuration
Additionaly, priority spread is disabled in the basic scheduler (prio_spread = 1) through the ODP configuration file (see ODP_CONFIG_FILE)

$ cat odp_perf.conf
odp_implementation = "linux-generic"
config_file_version = "0.1.19"

sched_basic: {
prio_spread = 1
}
IPv4 Forwarding with 64-byte frame	Throughput (mpps)
	Multi packet API	Single packet API
1 core	3.45	3.44
2 cores	9.10	9.01
3 cores	13.53	13.60
4 cores	14.73	14.72

Default configuration
IPv4 Forwarding with 64-byte frame	Throughput (mpps)
	Multi packet API	Single packet API
1 core	1.52	1.66
2 cores	2.71	2.91
3 cores	5.01	6.23
4 cores	7.20	8.02
5 cores	9.16	9.25

# Use-case: UDP Forwarding
## Test description
UDP traffic is sent from a packet generator (node 1) to multiple destination sockets on node 2, running the NFP application. The traffic is then forwarded to node 3 (on a single UDP port).

fp0	fp1
2
1

3

192.168.100.10 192.168.100.20:5001[,500X]	192.168.200.20:5000
Note:
- ‘nfp_udp_fwd_socket’ example is used
- TX and RX operations are performed in ‘direct mode’
- RSS is enabled on RX
- Burst TX mode enabled by default
## Configurations
Name	Description
NFP Extended pool	Configuration applied through configuration file (NFP_CONF_FILE): / nfp_global_param: { / pkt_pool: { / nb_pkts = 262143 / } / }
NFP UDP performance	Configuration applied through configuration file (NFP_CONF_FILE): / nfp_global_param: { / pkt_pool: { / nb_pkts = 262143 / } / udp: { / pcb_hashtbl_size = 1000 / pcbport_hashtbl_size = 1000 / } / } / Additionally, the following build time flags are applied: / - NFP_STATIC_SOCKET_CONFIG / - NFP_INP_LOCK_DISABLED
NFP IPv4 Hook	Configuration applied through configuration file (NFP_CONF_FILE): / nfp_global_param: { / pkt_pool: { / nb_pkts = 262143 / } / udp: { / pcb_hashtbl_size = 1000 / pcbport_hashtbl_size = 1000 / } / } / Additionally, IPv4 Local hook is used to forward packets.

## Results
NFP Extended pool configuration
UDP Forwarding, 64B frame	Throughput (mpps)
	1 socket		2 sockets		4 sockets
	Multi	Single	Multi	Single	Multi	Single
1 core	1.80	1.73	1.80	1.72	1.82	1.68
2 cores	2.93	1.83	2.53	1.91	207	1.87
3 cores	2.87	1.70	3.06	2.02	3.00	1.88
4 cores	3.99	2.00	4.28	2.15	4.00	2.37

NFP UDP performance configuration
UDP Forwarding, 64B frame	Throughput (mpps)
	1 socket	2 sockets	4 sockets	11 sockets	100 sockets
	Multi	Multi	Multi	Multi	Multi
1 core	1.82	1.81	1.80
2 cores	2.93	2.77	2.34
3 cores	3.91	3.88	3.82
4 cores	5.49	5.24	5.22
11 cores				8.86	8.76

NFP IPv4 hook
UDP Forwarding, 64B frame	Throughput (mpps)
	Multi	Single
1 core	2.12	2.68
2 cores	4.92	4.94
3 cores	9.97	12.75
4 cores	14.61	14.26

# Use-case: UDP Termination
## Test description
UDP packets are sent from the packet generator on node 2 to a single socket on node 1. The packets are terminated on a single control thread via POSIX or channel API.

1
2

192.168.100.30:5001 192.189.100.10
This case corresponds to the scenario when specific data flow needs special processing on a control thread.
Note:
- ‘nfp_udp_term_socket’ example is used
- TX and RX operations are performed in ‘direct mode’
- RSS is enabled on RX
- UDP traffic: 64B frame (10B UDP payload), 65000 source ports
- On Channel API, enqueue is multi-thread safe, dequeue is multi-thread unsafe
- A single core is preforming UDP termination while multiple cores are performing packet processing
## Configurations
Name	Description
NFP Extended pool	Settings applied through configuration file (NFP_CONF_FILE): / nfp_global_param: { / pkt_pool: { / nb_pkts = 262143 / } / }

## Results
NFP Extended pool configuration
Description:
- POSIX: UDP termination is performed with POSIX API
- Channel (Take): UDP termination is performed with Channel API, using packet ‘take’ method and no user data

Cores	UDP termination (mpps)
	Multi packet processing API		Single packet processing API
	POSIX	Channel / (Take)	POSIX	Channel / (Take)
1 core	3.77	3.18	1.93	2.86
2 cores	3.73	5.35	1.83	3.01
4 cores	1.73	5.75	1.95	3.88
8 cores	0.53	4.18	0.82	3.79

Note: The performance is limited by the processing capacity of the single termination thread and the utilization of socket framework on input.
# Use-case: UDP classification and termination
UDP packets are sent from the packet generator on node 2 to node 1. The traffic classification is used to direct targeted traffic (UDP port 54321) to a specified worker thread where is processed. Finally, traffic is terminated using POSIX or channel API on a control thread.

1
2

192.168.100.30:54321 192.189.100.10
This case corresponds to the scenario when specific data flow needs special processing on a control thread.
Note:
- ‘nfp_classification’ example is used
- TX operation is performed in ‘direct mode’
- RX operation is performed in ‘scheduler mode’
- UDP traffic: 64B frame (10B UDP payload), 65535 source ports
- On Channel API, TX and RX are multi-thread unsafe
- A single (worker thread) core is processing the classified traffic (core #2)
- A single (control thread) core is preforming UDP termination (core #1);
- Multi-packet (packet vector) processing API is used in both cases (POSIX and channel API termination)
## Configurations
Name	Description
NFP Extended pool	Settings applied through configuration file (NFP_CONF_FILE): / nfp_global_param: { / pkt_pool: { / nb_pkts = 262143 / } / }

## Results
NFP Extended pool configuration
Cores	UDP termination (mpps)
	Multi packet processing API
	POSIX	Channel / (Take)
1 cores	4.97	7.22

# Use-case: web server
## Test description
HTTP request are generated with a 3rd party application (httperf), one request per TCP connection. NFP reads the requested file and sends the response.

1
2

192.168.100.30:2048 192.189.100.10

Note:
- ‘nfp_webserver2’ example is used
- TX and RX operations are performed in ‘direct mode’
- RSS is enabled on RX
## Configurations
Name	Description
Webserver configuration	Configuration applied through configuration file (NFP_CONF_FILE): nfp_flv_webserver.conf / nfp_global_param: { / evt_rx_burst_size = 32 / pkt_tx_burst_size = 32 / chksum_offload: { / ipv4_rx_ena = true / udp_rx_ena = true / tcp_rx_ena = true / ipv4_tx_ena = true / udp_tx_ena = true / tcp_tx_ena = true / } / socket: { / num_max = 65535 / sd_offset = 0 / } / tcp: { / pcb_tcp_max = 65535 / } / }

## Results
Webserver configuration
Webserver2	Connection rate (connection/s)
	Multi packet API	Single packet API
1 core	43000	41000
2 cores	53000	53000
3 cores	53000	53000
4 cores	53000	54000